## Slide 1: EE 272 Digital Systems Fall 2019 Instructor: Dr. Aashir Waleed
Lecture 7a – 1
Chapter 6 Registers

## Slide 2: Lecture Overview
Lecture 7a – 2
 Parallel Registers – a group of flip-flops in parallel
 Shift registers - a group of flip-flops in series
 Use of registers
 In communication
 In addition
 Reading Assignments:
 Chapter 6 of Textbook

## Slide 3: Registers
Lecture 7a – 3
 Registers are groups of flip-flops
 Basic parallel storage register:
 – Store N-bit information
 – Each FF stores one-bit
A 4-bit register:
clk
Register symbol
Parallel Inputs
Parallel Outputs

## Slide 4: Register – Timing Waveforms
Lecture 7a – 4

## Slide 5: Register with Asynchronous Clear
Lecture 7a – 5
 Registers, just like flip flops, can have additional Clear (reset) and Set (Preset) inputs
 Clear – clear the output to 0
 Set – Set the output to 1
 Could be active low or active high
 Active low – Clear = 0 (set = 0) means clear (set) the output to 0 (1)
 Active high – Clear = 1 (set = 1) means clear (set) the output to 0 (1)
 Asynchronous clear or set – change the output of the register immediately, do not need to wait for the clock edge.

## Slide 6: E.g. 4-bit Register with Asynchronous Clear
Lecture 7a – 6
Timing waveform
Implementation using Flip-flops with asynchronous clear

## Slide 7: Asynchronous vs. synchronous inputs
Lecture 7a – 7
Asynchronous clear has an immediate effect, do not need to wait for the clock
Synchronous clear changes the output after the next clock edge, basically, the flip flops just load a “ZERO” to the output at the next clock edge
  This example show active LOW clear signal. Active HIGH can also be used. How can you do it?

## Slide 8: Registers with Parallel Load
Lecture 7a – 8
 Load (or enable) signal to control whether the data is to be loaded into the register in the next clock edge
 For active HIGH, if load (enable) = 1, the input data will be loaded and stored in the register at the coming clock edge, otherwise no change at the output at the clock edge.
 Load is a synchronous input, i.e. effect at the output only happen at the next clock edge.
symbol
Timing waveform

## Slide 9: Implementation of 1-bit “Register with Load” using D-Flip Flop and Mux
Note that DFF simply loads old value when LOAD = 0.
DFF is loaded every clock cycle.

## Slide 10: 4-bit register with Load (Enable)
Lecture 7a – 10

## Slide 11: Timing Waveform of a 8-bit register with load and asynchronous clear

## Slide 12: Shift register
Lecture 7a – 12
CLK
Q’
Cascading of flip-flops in series to form a shift register
– New value to first stage while the second stage obtains current value of the first stage
» Shift function (in-series arrangement)
» Storage function (by flip-flop)
IN D Q Q0 D Q Q1
Q’
IN Q0 Q1 CLK
100

## Slide 13: 4-bit Shift Register
Lecture 7a – 13
Shift
Shift Shift
Q1 1 | Q 2 0 | Q 3 0 | Q4 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1

## Slide 14: Parallel Input Serial Output (PISO) shift register
 Specifications:, e.g.
 – 6 bits
 – Rising edge triggered
 – Loaded (synchronously) when load = ‘1’
 – Data shifted-out LSB first

## Slide 15: Shift Register Timing Waveforms
Lecture 7a – 15

## Slide 16: Universal Shift Register
Lecture 7a – 16
Combinate combinational and sequential circuits for more functions
  Support shift in both direction
  Support both shifts and parallel-load capabilities

## Slide 17: Universal Shift Register (Cont’d)
Lecture 7a – 17
S1 S0
0 0  Keep Data
1  Shift Right
0  Shift Left
1 1  Parallel Load

## Slide 18: Application example–data transfer
Lecture 7a – 19
 Parallel data transfer
 Multiple number of bits are transferred from one place to another (e.g. from one processor to the other processor)
 Use parallel registers in the source and destination
 Requires a lot of lines between the sources and destination, that may be expensive especially if the distance is long and the speed of transfer is high

## Slide 19
Lecture 7a – 20
Application example–serial data transfer
 To reduce the number of parallel wires, we can transfer data in serial fashion, i.e. one bit at a time.