## Slide 1: EE272 Digital Systems Fall 2019 Instructor: Dr. Aashir Waleed
Lecture 2 – 1
Chapter 2
Boolean Algebra & Logic Gates

## Slide 2: Lecture Overview
Lecture 2 – 2
 Boolean Algebra
 Boolean Functions
 Logic Gates
 Implementing Boolean Functions using Logic Gates
 Canonical and Standard Forms
 Inside logic gates
 TTL and CMOS logic
 Electrical characteristics: Signal levels, Noise margins, Fan- out, Speed
 Reading assignment: Chapter 2.1 to 2.8

## Slide 3: Logic function
Lecture 2 – 3
 A,B, C,Y – logic variables (binary signals)
 A, B,C – inputs
 Y – output
 Logic function:Y = F(A,B,C)
 Digital system works on binary number which has only two elements, ‘0’, and ‘1’
 Need circuits to manipulate 1’s and 0’s, they are called logic function
A
B C
Y
F

## Slide 4: Truth Table
Lecture 2 – 4
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 Tabulate all possible input combinations of the variables
 Showing the relation between the values that the variables may take and the result of the operation
 E.g.
How can we design a circuit that implement a certain function specified by a truth table?

## Slide 5: Boolean Algebra
Lecture 2 – 5
 In 1854, a mathematician, George Boole, in a book called “An Investigation of the Laws of Thought, on Which are Founded the Mathematical Theories of Logic an Probabilities” developed an algebraic system to handle only two variables,TRUE and FALSE

## Slide 6: Structure of Boolean Algebra
Lecture 2 – 6
 a set of elements B
 Two binary operations
 One unary operation
{AND, OR}  { , + }
{NOT}  { ' }
 Axioms (Huntington Postulates)
 1. Set B contains at least two elements, a, b, such that a  b
 consider a two valued Boolean algebra, i.e. B = {0,1}
 2. Closure (with respect to the Binary operator +, •):
 (i) a + b is in B (ii) a • b is in B
 3. Commutative Laws:
 (i) a + b = b + a (ii) a • b = b • a
 4. Identity elements with respect to the Binary operator: 0, 1 in B
(ii) a • 1 = a
(ii) a • (b + c) = a • b + a • c
 (i) a + 0 = a
 5. Distributive Laws:
 (i) a + (b • c) = (a + b) • (a + c)
 6. Complement:
 (i) a + a' = 1
(ii) a • a' = 0

## Slide 7: Laws of Boolean Algebra
Lecture 2 – 7
 Duality:
 A dual of a Boolean expression is derived by interchanging OR and AND operations, and 0s and 1s (literals are left unchanged)
 Any law that is true for an expression is also true for its dual.
 Theorems of Boolean Algebra derived from postulates
 Operations with 0 and 1:
x 0 = 0
x x = x
(x y)’ = x’ + y’
x (x + y) = x
 x + 1 = 1
 Idempotent:
 x + x = x
 Involution:
 (x’)’ = x
 De Morgan:
 (x + y)’ = x’ y’
 Absorption:
 x + xy = x
 Associative:
 (x + y) + z = x + (y + z)
(x y) z = x (y z)

## Slide 8: Proving Theorems via axioms of Boolean Algebra
Lecture 2 – 8
 Theorems can be proved (derived) by axioms
 Example 1: prove the simplification theorem: x y + x y’ = x
 x y + x y’ | = x (y + y’) | distributive law
 x (y + y’) | = x (1) | complementary law
 x (1) | = x | identity
 Example 2: prove the Simplification theorem: x + x y = x
 x + x y  x 1 + x y | = x 1 + x y = x (1 + y) | identity distributive law
 x (1 + y) | = x (1) | identity
 x (1) | = x | identity
 In theory, simplification should be done by these laws
 In practice, graphic method is used for convenience
 How does these Boolean Algebra relate to digital design?

## Slide 9: Laws of Boolean Algebra (Cont.)
Lecture 2 – 9
 Distributive Laws:
 x (y + z) = (x y) + (x z)
 “Simplification” Theorems:
 x y + x y’ = x
x (y + y’) = x 1 = x
Since y + y’ = 1
 x + x y = x
x(1 + y) = x
Since 1 + y = 1
 (x + y’) y = x y
xy + y’y = xy since y’y = 0
 DeMorgan’s Law:
 (x + y + z + …)’ = x’ y’ z’
x +(y z) = (x + y)(x + z)
(x + y) (x + y’) = x
x x + x y’ + yx + yy’ = x (1 + y’ + y) = x Since x x = x and yy’ = 0 also 1 + y’ + y = 1
x (x + y) = x
x x + x y = x (1 + y) = x
(x y’) + y = x + y
(x + y ) (y’ + y) = x + y since y’ + y =1
(x y z …)’ = x’ + y’ + z’ + …

## Slide 10: More example on DeMorgan’s Law
Lecture 2 – 10
 Complement of a Function
 F= (A+B+C)’ = (A+x)’ where x = B+C
 => F = A’x’
 => F= A’(B+C)’
 => F = A’(B’C’) = A’B’C’
 We can generalize F = (A+B+C+…+Z)’=A’B’C’…Z’
 Similarly
 F=(ABC)’=(Ax)’ where x = BC
 =>F=A’+x’
 =>F = A’+(BC)’
 =>F = A’+B’+C’
 And we have F = (ABC…Z)’ = A’+B’+C’+…+Z’

## Slide 11:  Theorems for Multiplying and Factoring:
Lecture 2 – 11
 (x + y) (x’ + z) = x z + x’ y
 x x’ + x z + y x’ + y z = x z + x’ y
 x z + y x’ + y z = x z + x’ y since x x’ = 0
 x z + y x’ + y z ( x + x’) = x z + x’ y since x + x’ = 1 and y z 1 = y z
 x z + y x’ + y z x + y z x’ = x z + x’ y
 x z (1 + y) + y x ‘ (1 + z ) = x z + x’ y
 x z 1 + y x’ 1 = x z + x’ y since 1 + y = 1 and 1 + z = 1
 x y + x’ z = (x + z) (x’ + y)
 (x y + x’ ) (x y + z) = (x + z) (x’ + y)
 (x + x’)(y + x’)(x + z)(y + z) = (x + z)(x’ + y)
 (y + x’)(x + z)(y + z + x x’) = (x + z)(x’ + y) since x + x’ = 1 and x x’ = 0
 (y + x’)(x + z)(y + z + x)(y + z + x’) = (x + z)(x’ + y)
 [(y + x’)(y + x’) + z (y + x’)][(x + z)(x + z) + (x + z) y ] = (x + z)(x’ + y)
 [(y + x’)(1 + z)][(x + z)(1 + y)] = (x + z)(x’ + y) since 1 + z = 1 and 1 + y = 1

## Slide 12:  Consensus Theorem:
Lecture 2 – 12
 x y + y z + x’ z = x y + x’ z
 Proof?
 (x + y) (y + z) (x’ + z) = (x + y) (x’ + z)
 Proof?

## Slide 13: Digital Logic Circuits
Lecture 2 – 13
 In 1938, Claude Shannon (father of information theory) showed (in his Master’s thesis!) how to map Boolean Algebra to digital circuits (using electromechanical relays)
 to optimize arrangements of telephone routing switches using laws of Boolean Algebra
 to use arrangements of switches to solve logic problems
 Today we use the same principles, but replace electromechanical relays with logic gates (made of transistors).

## Slide 14: Two-valued Boolean Algebra and Basic Logic gates
 B = {0,1}
 Two binary operators + (OR), . (AND)
 Complementary operator (‘)
Not gate (inverter)
A | Y = A’
0 | 1
1 | 0
AND gate
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR gate
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
INVERTER
AND
OR

## Slide 15: Example: three-input function
Lecture 2 – 15
 Logic Function: F = x.(y+z)
 Truth table Circuits (Schematic diagram)
x | y | z | (y+z) | F=x.(y+z)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
y z
x
F
Literal – a single variable within a term (complemented or un- complemented). For example: x, y, z are all literals

## Slide 16: Generalization to any function (gate)
Lecture 2 – 16
A | B | Y = ?
0 | 0 | Y0
0 | 1 | Y1
1 | 0 | Y2
1 | 1 | Y3
ANY gate Y0, Y1, Y2, Y3 assumes either 0 or 1
To generalize, we define “minterms” and “maxterms”
Minterms are PRODUCT terms
Maxterms are SUM terms
A | B | Y | Minterms
0 | 0 | Y0 | A’ B’
0 | 1 | Y1 | A’ B
1 | 0 | Y2 | A B’
1 | 1 | Y3 | A B
A | B | Y | Maxterms
0 | 0 | Y0 | A + B
0 | 1 | Y1 | A + B’
1 | 0 | Y2 | A’ + B
1 | 1 | Y3 | A’ + B’

## Slide 17: Generalization by using MINTERMS
Lecture 2 – 17
A | B | Y | Minterms
0 | 0 | Y0 | A’ B’
0 | 1 | Y1 | A’ B
1 | 0 | Y2 | A B’
1 | 1 | Y3 | A B
Y = Y0A’B’ + Y1A’B + Y2AB’ + Y3AB
This is also known as the SUM of PRODUCTS (SOP) form of the function Y
Let’s put to test on AND and OR gates
AND gate
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Y = 0 A’B’ + 0 A’B + 0 AB’ + 1 AB = AB
OR gate
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Y = 0 A’B’ + 1 A’B + 1 AB’ + 1 AB
= A’B + AB’ + AB
Does this look like OR gate?
How about after further simplification:
= A’B + AB’ + AB + AB
= B (A’ + A) + A (B’ + B)
= A + B

## Slide 18: Further notation on MINTERMS (Σm):
Lecture 2 – 18
A | B | Y | Minterms
0 | 0 | Y0 | m0=A’ B’
0 | 1 | Y1 | m1=A’ B
1 | 0 | Y2 | m2=A B’
1 | 1 | Y3 | m3=A B
Y = Y0A’B’ + Y1A’B + Y2AB’ + Y3AB
This is also known as the SUM of PRODUCTS (SOP) form of the function Y
Let’s put to test on AND and OR gates
AND gate
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Y = AB =Σm(3) = m3
OR gate
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Y = A’B + AB’ + AB
= Σm(1,2,3) = m1 + m2 + m3
Does this look like OR gate?
How about after further simplification:
= A’B + AB’ + AB + AB
= B (A’ + A) + A (B’ + B)
= A + B

## Slide 19: Generalization by using MAXTERMS
Lecture 2 – 19
Y = (Y0+A+B)(Y1+A+B’)(Y2+A’+B)(Y3+A’+B’)
This is also known as the PRODUCT of SUMS (POS) form of the function Y
Let’s put to test on AND and OR gates
OR gate
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Y | Maxterms
0 | 0 | Y0 | A + B
0 | 1 | Y1 | A + B’
1 | 0 | Y2 | A’ + B
1 | 1 | Y3 | A’ + B’
Y = (0+A+B)(1+A+B’)(1+A’+B)(1+A’+B’) = A + B
AND gate Y
= (0+A+B)(0+A+B’)(0+A’+B)(1+A’+B’)
= (A + B)(A + B’)(A’ + B)
Does this look like OR gate?
How about after further simplification:
=(AA + AB’ + BA + BB’)(A’ + B)
=A(1 + B’ + B)(A’ + B) since AA = A and BB’=0
=AA’+AB since AA’ = 0
=AB

## Slide 20: Further notation on MAXTERMS (ΠM):
Lecture 2 – 20
Y = (Y0+A+B)(Y1+A+B’)(Y2+A’+B)(Y3+A’+B’)
This is also known as the PRODUCT of SUMS (POS) form of the function Y
Let’s put to test on AND and OR gates
OR gate
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Y | Maxterms
0 | 0 | Y0 | M0 =A + B
0 | 1 | Y1 | M1 =A + B’
1 | 0 | Y2 | M2 = A’ + B
1 | 1 | Y3 | M3 = A’ + B’
Y = A + B = ΠM(0) = M0
AND gate Y
= (A + B)(A + B’)(A’ + B)
= ΠM(0,1,2) = M0
M1 M2
Does this look like OR gate?
How about after further simplification:
=(AA + AB’ + BA + BB’)(A’ + B)
=A(1 + B’ + B)(A’ + B) since AA = A and BB’=0
=AA’+AB since AA’ = 0
=AB

## Slide 21: Apply to previous Example: F = x (y + z)
 SOP: F = Σ m(5,6,7) = m5 + m6 + m7 = x y’ z + x y z’ + x y z
 POS: F = Π M(0,1,2,3,4) = M0 M1 M2 M3 M4

= (x + y + z)(x + y + z’)(x + y’ + z)(x + y’ + z’)(x’ + y + z)
x | y | z | (y+z) | F = x.(y+z) | Minterms | Maxterms
0 | 0 | 0 | 0 | 0 | m0 = x’ y’ z’ | M0 = x + y + z
0 | 0 | 1 | 1 | 0 | m1 = x’ y’ z | M1 = x + y + z’
0 | 1 | 0 | 1 | 0 | m2 = x’ y z’ | M2 = x + y’ + z
0 | 1 | 1 | 1 | 0 | m3 = x’ y z | M3 = x + y’ + z’
1 | 0 | 0 | 0 | 0 | m4 = x y’ z’ | M4 = x’ + y + z
1 | 0 | 1 | 1 | 1 | m5 = x y’ z | M5 = x’ + y + z’
1 | 1 | 0 | 1 | 1 | m6 = x y z’ | M6 = x’ + y’ + z
1 | 1 | 1 | 1 | 1 | m7 = x y z | M7 = x’ + y’ + z’

## Slide 22: Apply to previous Example: F = x (y + z)
 SOP: F = Σ m(5,6,7) = m5 + m6 + m7 = x y’ z + x y z’ + x y z
 Show that if you simplify SOP you get x (y + z)???
 ….
 POS: F = Π M(0,1,2,3,4) = M0 M1 M2 M3 M4

= (x + y + z)(x + y + z’)(x + y’ + z)(x + y’ + z’)(x’ + y + z)
Show that if you simplify POS, you get x (y + z)???
…

## Slide 23: Minterms/Maxterms complement each other
Lecture 2 – 23
One can be derived from the other by applying DeMorgan’s Law Example:
m5 = x y’ z  M5 = m5’ = [x y‘z]’= x’+ y + z’
M2 = x + y’+ z  m2 = M2’ = [x + y’+ z]’= x’ y z’
x | y | z | Minterms | Maxterms
0 | 0 | 0 | m0 = x’ y’ z’ | M0 = x + y + z
0 | 0 | 1 | m1 = x’ y’ z | M1 = x + y + z’
0 | 1 | 0 | m2 = x’ y z’ | M2 = x + y’ + z
0 | 1 | 1 | m3 = x’ y z | M3 = x + y’ + z’
1 | 0 | 0 | m4 = x y’ z’ | M4 = x’ + y + z
1 | 0 | 1 | m5 = x y’ z | M5 = x’ + y + z’
1 | 1 | 0 | m6 = x y z’ | M6 = x’ + y’ + z
1 | 1 | 1 | m7 = x y z | M7 = x’ + y’ + z’

## Slide 24: How to go from specification (truth table) to circuits?
 Get the truth table and SOP or POS from truth table
 Carry out logic minimization
 We will look into how we can do it systematically
 Then map the logic expression with gate.

## Slide 25
Lecture 2 – 25
Sum of Product (Minterm expansion)
Example
F(A,B,C)  m(3,4,5,6,7)  m3  m4  m5  m6  m7

## Slide 26: SOP minimization and gate implementation
Lecture 2 – 26
 A function might have many alternative Boolean expressions
 But only one minimized Boolean expression
F = A’BC + AB’C’ + AB’C + ABC’ + ABC
= A B' (C + C') + A' B C + A B (C' + C)
= A B' + A' B C + A B
= A (B' + B) + A' B C
= A + A' B C
= A + B C
B
C
A
F

## Slide 27
Lecture 2 – 27
Product of Sum (Maxterm expansion)
F(A, B, C) M (0,1, 2)  (A  B  C)(A  B  C ')(A  B ' C)
Then POS minimization and gate implementation Show that the minimized form: F = (A+B) (A+C)

## Slide 28: Summary
Lecture 2 – 28
 Four Alternative Implementations of F =m(3,4,5,6,7) :
A
B
F2
F3
F4
F1
C
Canonical Sum of Minterms
F1 = A' B C + A B' C' + A B' C
+ A B C' + A B C
Minimized Sum of Minterms F2 = A + BC
Canonical Products of Maxterms
F3 = (A+B+C) (A+B+C') (A+B'+C)
Minimized Products of Maxterms F4 = (A+B) (A+C)

## Slide 29: Summary
Lecture 2 – 29
 Truth table and Boolean expression
 Truth table is the unique signature of a Boolean function
 Many alternative expressions (gate realizations) may have the same truth table
 Canonical form: Standard form for a Boolean expression
 Provides a unique algebraic signature because it derives from the truth table
 Either presented in SOP or POS form
 All the terms in SOP or POS must contain all the literals that the function depends on (because it’s Canonical)
 Leads to a two-level gate implementation (see the previous slide)
 Sum of Product (AND first, OR last)
 also known as minterm expansion
 Product of Sum (OR first,AND last)
 Also known as maxterm expansion

## Slide 30: Two-Level Canonical Forms (SOP or POS)
Lecture 2 – 30
 Minterms
 Maxterms

## Slide 31: Two-Level Canonical Forms (Cont’d)
Lecture 2 – 31
 From Maxterm to Minterms
 Express Complementary of F in Maxterms
 F' = (A + B' + C') (A' + B + C) (A' + B + C') (A' + B' + C) (A' + B' + C')
 Apply DeMorgan's Law to obtain F
 (F')' = {(A + B' + C') (A' + B + C) (A' + B + C') (A' + B' + C) (A' + B' + C')}’
 F = A' B C + A B' C' + A B' C + A B C' + A B C
 From Minterm to Maxterms
 Express Complementary of F in Minterms
 F' = A' B' C' + A' B' C + A' B C’
 Apply DeMorgan's Law to obtain F
 (F')' = (A' B' C' + A' B' C + A' B C')’
 F = (A + B + C) (A + B + C') (A + B' + C)

## Slide 32: Logic circuits and Boolean expression
Lecture 2 – 32
D
 Same function can have different Boolean expression and hence different gate implementation
 Example: F = AB+C(D+E) = AB +CD +DE
 Same function F, but different expression and hence different gate implementation
F3 = AB + CD + DE
F3 = AB + C(D +E)

## Slide 33: About Boolean Algebra
Lecture 2 – 33
 Boolean algebra provides a mathematical foundation for manipulating Boolean expressions. With Boolean algebra, we are able to simplify (or minimize or optimize) a Boolean expression, which leads to a simplified (or minimized or optimized) circuit
 In practice, we rarely do it by manual algebraic manipulation, but use other methods for simplifying Boolean expressions (next week!). For simple combinational logic, the most common method for simplifying Boolean expression is a Karnaugh Map (K-Map). For more complex and multi-level combinational logic, computer-aided-design (CAD) algorithms are used, e.g. Quine-McCluskey, Espresso, etc. Different applications use different algorithms.

## Slide 34: Incompletely Specified Functions
Lecture 2 – 34
 A n-input functions have 2n input combinations
 But for a given function, not all input combinations are specified
 Example, Binary Coded Decimal Digit Increment by 1
 BCD digits encode the decimal digits 0 - 9 in the bit patterns of 0000 - 1001
 6 out of 16 possible are not defined
A B C D W X Y Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X
1 | 1 | 0 | 0 | X | X | X | X
1 | 1 | 0 | 1 | X | X | X | X
1 | 1 | 1 | 0 | X | X | X | X
1 | 1 | 1 | 1 | X | X | X | X
Off-set of W
On-set of W
Don't care (DC) set of W
These input patterns should never be encountered in practice
associated output values are "Don't Cares"

## Slide 35: Incompletely Specified Functions
Lecture 2 – 35
 Canonical Representations of the BCD Increment by 1 Function:
 Minterms
 Z = m0 + m2 + m4 + m6 + m8 + d10 + d11 + d12 + d13 + d14 + d15
 Z = m(0, 2, 4, 6, 8) + d(10, 11, 12 ,13, 14, 15)
 W = m(7, 8) + d(10, 11, 12 ,13, 14, 15)
 X = m(3, 4, 5, 6) + d(10, 11, 12 ,13, 14, 15)
 Y = m(1, 2, 5, 6) + d(10, 11, 12 ,13, 14, 15)
 Maxterms
 Z = M1 • M3 • M5 • M7 • M9 • D10 • D11 • D12 • D13 • D14 • D15
 Z = M(1, 3, 5, 7, 9) • D(10, 11, 12, 13, 14 ,15)
 W =
 X =
 Y =

## Slide 36: More Logic Functions
Lecture 2 – 36
For a 2-input function, there are 22 = 4 input combinations
and 24 = 16 output functions
 16 Boolean functions of two variables
 2 variables
 2 identities
X,Y
0, 1
 4 primitive functions X',Y', X•Y, X+Y
(AND, OR, NOT)
 2 CMOS building blocks
 2 equality/inequality gates
(X+Y)’, (X•Y)’ XY, (XY)’
(NAND, NOR) (XOR, XNOR)
 4 inhibition and implication function
(for comparison, too)
X•Y
XY (X+Y)’ Y’
X | Y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 |  |  |  | X |  | Y |  |  | X+Y (XY)’ |  |  |  | X’ |  | (X • |  | Y)’ 1

## Slide 37: Logic Functions: XOR, XNOR
Lecture 2 – 37
Boolean expression
– X  Y = X Y' + X' Y
Boolean expression
– (X  Y)’ = XY + X' Y’
XOR Gate:
  Z=1 if X  Y (inequality gate)
  Z=1 if only X or Y = 1
» odd function
Gate symbol
X Y
Truth table
X Y
XNOR Gate:
  Z=1 if X = Y (equality gate)
  Z=1 if none or both X,Y=1
» even function
Gate symbol
Z
X | Y | Z Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth table | X | Y | Z
 | 0 | 0 | 1
 | 0 | 1 | 0
 | 1 | 0 | 0
 | 1 | 1 | 1

## Slide 38: Common 2-input Logic Gates
Lecture 2 – 38

## Slide 39
Lecture 2 – 39
2-input and 3-input Logic Gates
3-input OR gates could be made by 2 2-input OR gates
  By associate law x + y + z = (x+y) + z = x + (y+z)
  output equals to 1 if any input is 1
z
Could 3-input NOR gate be made by 2 2-input NOR gates?
  Associate law applies to primitive gates, but not to NOR gates
– [(x+y)’+z]’ = (x+y)  z’ = xz’ + yz’  (x+y+z)’
  output equals to 0 if any input is 1

z


## Slide 40: Sequence of designing a digital circuit given the logic function
 Design Sequence:
 1.Truth Table (input and output relations)
 Derive truth table from project specifications
 2. Boolean Expressions
 Derived from the truth table
 3.Logic Minimization
 Use Laws of Boolean Algebra to reduce the complexity of Boolean expressions while maintaining the same function
 2’ Graphic Method (K-Map) (Chapter 3)
 Re-express the truth table in graphs (K-Map)
 3’ Logic Minimization
 READ the simplified Boolean expressions from the graphs
 4. Digital Circuit
 Map the simplified Boolean expressions to digital circuits
 5. Waveforms
 CAD tool simulation and experiments

## Slide 41
Lecture 2 – 41
Reading assignment
 Chapter 2.1 to 2.8 of textbook